## Slide 1: Evolution of Microprocessor

## Slide 2: Intel 4004
Introduced in 1971
16-pin ceramic dual-in-line package.
2,300 transistors
4 bit architecture
clock frequency : 740KHz.
Used for calculators
Instruction Set : 46
It was able to address 640 bytes of RAM and 4096 bytes of ROM.

## Slide 3: Intel 4040
Introduced in 1974
3000 transistors
Maximum clock frequency of 740KHz.
Instruction set: 60
Program memory : 8KB (13-bit address space).
24-pin dual-in-line package.

## Slide 4: Intel 8008
First 8-bit microprocessor
Introduced in 1972.
3500 transistors.
14-bit address bus (16KB)
First commercial non-calculator PC.
18-pin dual-in-line package.
Instruction Set: 48
Clock speed was from 0.2MHz to 0.8MHz.

## Slide 5: Intel 8080
Introduced in 1974.
Used same instruction set of 8008
4500 transistors.
40-pin dual-in-line package
16-bit address bus(64KB)
Maximum Clock Frequency : 2MHz.

## Slide 6: Intel 8085
It was introduced in 1977.
“5” implies +5V power supply.
6500 transistors
40-pin dual-in-line package
16-bit address bus (64KB) and 8-bit data bus.
74 instructions
Clock Speed: 3, 5 and 6MHz

## Slide 7: Intel 8086
It was introduced in1978
40-pin dual-in-line package
16-bit microarchitecture
20-bit address bus (1 MB)
16-bit data bus
Instruction set : 117
approximately 20,000 transistors
Clock Speed: 5 to 10MHz

## Slide 8: Intel 8088
It was introduced in1979.
40-pin dual-in-line package.
16-bit microarchitecture
20-bit address bus (1 MB)
8-bit data bus
Instruction set : 117
approximately 20,000 transistors
Clock Speed: 5 to 10MHz

## Slide 9: Intel 8086/8088

## Slide 10: 8086
It is a 16-bit microprocessor.
It has a 16 bit data bus (it can read or write data to/from memory and ports either 16 bits or 8 bits at a time)
It has 20 bit address bus ( address 220 (1MB) locations).
  Each memory address represents a byte-wide location.

## Slide 11: 8086
Memory words is stored in two consecutive locations.
  If the first byte of a word is at even address, 8086 can read the entire word in one operation.
  If the first byte is at odd address, 8086 will read the first byte in one operation and the second byte in another operation.

## Slide 12: 8086 Architecture
8086 CPU is divided into two independent functional parts:
  Bus Interface Unit (BIU) and
  Execution Unit (EU).

## Slide 14: BUS INTERFACE UNIT
It handles all transfers of data and addresses on the buses for execution unit.
BIU
  sends out addresses
  fetches instruction from memory
  reads data from ports and memory and
  writes data to ports and memory.
Different parts of BIU are:
  Instruction Queue
  Segment Registers
  Instruction Pointer

## Slide 15: Instruction Queue
BIU fetches 6 instruction bytes ahead to speed up the execution.
Prefetched instruction bytes are stored in a FIFO group of registers called an instruction queue.
BIU fetches the instruction while EU decodes them.
Except in the cases of JUMP and CALL instructions, this method reduces the processing time.
This method of fetching the instruction while execution is in progress is called pipelining

## Slide 16: Segment Registers
BIU contains four 16-bit segment registers:
  code segment (CS) register
  stack segment (SS) register
  extra segment (ES) register and
  data segment (DS) register.
These registers hold the starting addresses of the four memory segments that 8086 is working with at a particular time.

## Slide 17: Instruction Pointer (IP)
This register holds the 16 bit address of the next code byte for the code segment.
The value in IP (referred as offset) is added to CS content to produce 20-bit address.
BIU has a dedicated adder for address computation.

## Slide 18: EXECUTION UNIT
EU tells BIU where to fetch instructions from as well as decode and execute instructions.
The execution unit includes the following parts.
  Control Circuitry
  Instruction Decoder
  Arithmetic and Logic Unit
  Flag Register
  General Purpose Registers
  Pointer and Index Register

## Slide 19: EXECUTION UNIT
Control Circuitry : directs the internal operations of the processor.
Instruction Decoder : It receives the fetched instruction from BIU and converts it into a series of action which the EU can carry out.
Arithmetic and Logic Unit: will do arithmetic and logical operations

## Slide 20: EXECUTION UNIT
Flag Register: It is a flip-flop which indicates some condition produced by the execution of an instruction or controls certain operations of the EU.
There are 6 conditional flags and 3 control flags
The contents of the 16-bit flag are as shown below.

## Slide 21: Flag Register
Conditional Flags
  reflect the results of previous operation involving ALU.
Flags | If the flag is set,
Carry Flag (CF) | there is a carry out of the MSB in addition operation or borrow is needed in a subtract operation.
Parity Flag (PF) | the result of an arithmetic or logical operation results in an even number of 1s in the binary representation
Auxiliary Carry (AF) | there is a carry out of the bit 3 position in an arithmetic operation
Zero Flag (ZF) | if the result of an arithmetic or logical operation is zero.
Sign Flag (SF) | if a signed arithmetic operation causes the MSB to 1. This implies that the number is negative.
Overflow Flag (OF) | when an arithmetic overflow has occurred. It indicates that the signed operation result will not fit in the destination.

## Slide 22: Flag Register
Control flags
  control the execution of special functions.
  These flags are set or reset with specific instructions used in the program
Flags | If the flag is set,
Direction Flag (DF) | the contents of the index register (SI and DI) will be decremented after each operation.
Interrupt Flag(IF): | the external maskable interrupt(INTR) is allowed to interrupt the program
Trap Flag(TF) | It is used for single stepping through the program. It is mainly used for debugging.

## Slide 23: Execution Unit
General Purpose Registers
EU has 4 general purpose registers labeled as AX, BX, CX and DX.
They are used as
  operands in most of the instructions
  source or destination registers during computation and transfer of data
  pointers to memory and
  counters.

## Slide 24: Execution Unit
Pointer and Index Register
The pointer and index registers are used to hold the offset within a segment.
They are
  Stack Pointer (SP) Register
  Base Pointer (BP) Register
  Source Index (SI) Register
  Destination Index (DI) Register.

## Slide 25: Operation of 8086/8088
When 8086/8088 is started,
  BIU outputs 20 bit address (from CS: IP ) onto the address bus causing the selected byte or word to be read into BIU
  IP is incremented by one to prepare for the next instruction fetch.
  Once inside BIU, the instruction is passed to Instruction Queue.

## Slide 26: Operation of 8086/8088
  If the queue is empty, the EU draws this instruction from the queue and begins execution
  While EU is executing the instruction, the BIU proceeds to fetch a new instruction.
  Depending on the execution time of the first instruction, BIU may fill the queue.
  BIU is programmed to fetch a new instruction whenever the queue has room for one or two additional bytes.

## Slide 27: 3 Conditions when EU has to wait
When an instruction requires access to a memory location not in queue
When the instruction is JUMP
When the instructions are slow to execute
  (AAM requires 83 clock cycles while instruction fetch requires 4 clock cycle)

## Slide 28: Difference b/w 8086 and 8088
 | 8086 | 8088
Data Bus Path | 16 bit | 8 bit
Instruction Queue Size | 6 bytes | 4 bytes

## Slide 29: Memory Segmentation
It is a powerful m/m management mechanism which allows programmers to partition their programs into modules that operate independently of one another.
8086 can access 1MB of memory. At any given time, it can work only with four 64KB segments
Segment register hold the upper 16-bits of the starting address called the segment base.
If CS register contains 1234H, then the code segment will start at 12340H address.

## Slide 30: Memory Segmentation
It uses two components to specify a memory location: a segment base and an offset
The offset of 8086 are 16-bit constants.
Size of offset limits the segment size
Physical address is obtained by multiplying segment base by 16 (shifting 4-bit left) and adding the offset address

## Slide 31: Memory Segmentation

## Slide 32: Memory Segmentation: Example

## Slide 33: Memory Segmentation