## Slide 2: 3 Conditions when BIU has to wait
When an instruction requires access to a memory location not in queue
When the instruction is JUMP/CALL
When the instructions are slow to execute
  (AAM requires 83 clock cycles while instruction fetch requires 4 clock cycle)

## Slide 3: Difference b/w 8086 and 8088
 | 8086 | 8088
Data Bus Path | 16 bit | 8 bit
Instruction Queue Size | 6 bytes | 4 bytes

## Slide 4: Programming model of 8086
There are fourteen 16-bit hardware registers divided into 5 groups:
  General Purpose Registers : AX, BX, CX, and DX
  Pointer and Index Registers : SP, BP, SI, and DI
  Segment Registers : CS, DS, ES, and SS
  Instruction Pointer : IP
  Flag Register : FR

## Slide 5: General Purpose Registers
They can be used as
  Operands
  Source or Destination registers
  Pointers
  Counters

## Slide 6: AX Register
It functions as Accumulator
It is the default operand in multiplication and division
It is divided into two parts – AH and AL. The higher 8-bit and lower 8-bit respectively

## Slide 7: BX Register
It functions as the Base register
It is used as a pointer to a memory location
It is suitable for accessing the elements of an array.
It can be treated as BH and BL

## Slide 8: CX Register
It functions as the Count register
Loop and repeat instructions use CX register to hold repeat count value
It can be treated as CH and CL

## Slide 9: DX Register
It functions as the Data register
It is used as an I/O address pointer in the IN and OUT instructions
It is also involved in 16-bit multiplication and division as default operand
It can be treated as DH and DL.

## Slide 10: Pointer and Index Registers
8086 has two pointer registers (SP and BP) and two index registers(SI and DI)
Pointer Registers are used for storing offset address of data in stack
Index Registers are used for storing index and offset of array elements

## Slide 11: SI Register (Source Index Register) DI Register (Destination Index Register)
They are used as a pointer to memory location
They are useful in accessing contiguous memory location, such as string
In repeat string instructions, SI is used as a pointer to a source string element and DI is used as a pointer to a destination string element

## Slide 12: Stack Pointer (SP) Register
This register is dedicated for maintaining an area of memory used as a stack
Stack Last-In-First-Out (LIFO)
Stack is useful in implementing procedure calls, recursions, passing of parameters, creation of local variables, etc.
SP always points to the top of the stack relative to SS

## Slide 13: PUSH
The process of storing data onto the stack
It is performed by the PUSH instruction.
Data is placed and SP is decremented by 2.
It is decremented by 2, because the stack system grows from higher to lower memory locations

## Slide 14: POP
The process of retrieving data from the stack
It is performed by POP instruction.
Data is retrieved and SP is incremented by 2
PUSH and POP are performed on 16-bit operands

## Slide 15: Base Pointer (BP) Register
It points relative to the stack segment register
It is generally used for accessing the parameters from the stack in the procedures
It is designed to provide support for passing of parameters between procedures, local variables and other stack based allocation and operations
It is used to access any location directly in the stack

## Slide 16: Instruction Pointer (IP) Register
It holds the offset of next instruction to be executed

## Slide 17: Segment Registers

## Slide 18: Code Segment (CS) Register
It points to the start of segment which contains the next instruction to be executed
The next instruction is pointed by CS:IP
8086 never fetches instruction from any segment other than that defined by CS:IP
It can be changed by instructions like far jump, far call and far return
It cannot be loaded directly
IP operates only relative to CS and no other registers operate relative to it

## Slide 19: Data Segment (DS) Register
It points to the start of the data segment.
It is not set to the data segment by default and user has to point to the appropriate segment.

## Slide 20: Stack Segment (SS) Register
It points to start of stack memory
The instructions which use SS:SP are push, pop, call and return

## Slide 21: Extra Segment (ES) Register
It is used for additional memory block for data storage
It is less efficient than the access in DS
It is extensively used in string instructions
It is used as the destination segment by ES:DI
It is useful in block copy, string comparison, memory scanning and cleaning block of memory locations

## Slide 22: Flag Register
It stores information about the status of processor and recently executed instruction
The format is
It is modified or read directly through processor control instructions such as CLD, STI, STD, etc. and through arithmetic and logical instructions
15 |  |  |  |  |  |  | 8 | 7 |  |  |  |  |  |  | 0
X | X | X | X | OF | DF | IF | TF | SF | ZF | X | AF | X | PF | X | CF

## Slide 23: Exercise
1010 0101 0000 1010 +
1110 0000 1010 1000
Perform this operation and write which all flags will be set

## Slide 24: Example to illustrate the setting of flags
Initially
CF = 0, PF = 0, AF = 0, ZF = 0, SF = 0, OF = 0
Operation is
1010 0101 0000 1010 +
1110 0000 1010 1000
---------------------------
1000 0101 1011 0010
After operation
CF = 1, PF = 1, AF = 1, ZF = 0, SF = 1, OF = 1

## Slide 25: Trap Flag (TF)
If TF is set, a trap (interrupt type 1) is executed after each instruction.
The CPU resets this flag while transferring control to the interrupt handler, if the interrupt is recognized.
There is no direct instruction to modify this flag
This feature is useful in implementing the program debugging utilities

## Slide 26: Interrupt Flag(IF)
If the interrupt enable flag is set, a maskable interrupt type can be recognized by the CPU; otherwise these interrupts are ignored
The CPU resets this flag while transferring control to the interrupt handler, if the interrupt is recognized

## Slide 27: Direction Flag(DF)
It is used for the manipulation of the data array in string instruction
It increments or decrements the index pointers based on the status of the direction flag.

## Slide 28: Memory Segmentation
It is a m/m management mechanism which allows programmers to partition their programs into modules that operate independently of one another.
At any given time, 8086 can work only with four 64KB segments
Segment register hold the upper 16-bits of the starting address called the segment base.
If CS contains 1234H, then the code segment will start at 12340H address.

## Slide 29: Memory Segmentation
It uses two components to specify a memory location: a segment base and an offset
The offset of 8086 are 16 bit constants.
Size of offset limits the segment size
Physical address is obtained by multiplying segment base by 16H (shifting 4-bit left) and adding the offset address

## Slide 30: Memory Segmentation

## Slide 31: Memory Segmentation: Example

## Slide 32: Memory Segmentation
The role of each segments are :
Data segment and extra segment holds the address of the data area.
Stack segment : system stack area.
Code segment : memory location where program is stored.
The offset addresses to be used are
  Instruction pointer (IP) : code segment
  Stack pointer (SP) : stack segment
  Base pointer (BP) : on stack and data
  Source Index (SI) and Destination Index (DI) : data and extra segment

## Slide 33: Advantages of Memory Segmentation
Multitasking
Protection (E.g. code can be write protected while data can have read and write access)
Relocation
One program can work on different sets of data. (by reloading DS register to point to the new data)

## Slide 34: Physical Memory Organization
1MB memory is organized as an odd bank and even bank, each of 512KB, addressed in parallel by the processor.
D7 – D0: Byte data with an even address is transferred
D15 - D8: odd address
Two signals and A0 for the selection of banks.